User Guide

# Introduction
Versa64Cart is designed to be a modern easy-to-use cartridge development board for Commodore 64 and Commodore 128 hobbyists and hackers. The versatile design of the PCB allows for flexible implementation of various cartridge types. Whether it’s a simple cartridge backup of an 8k game or a
switchable multi-program diagnostic cartridge, Vers64Cart has you covered.

# Overview

- Supported EPROMS:
  27C64 (8k), 27C128 (16k), 27C256 (32k), 27C512 (64k)
- Ability to access multiple program images by using optional on-board DIP switches (*)
- Rapid low-cost production of clean, single image cartridges via simple solder pad bridging option
- PCB designed to fit inside any standard C64 cartridge shell, including centre post versions
- Rounded corners to allow for easier cartridge insertion and reduced wear to PCB

# Setting #GAME and #EXROM
These are signals you must set to map a ROM into memory. They are routed to the C64 PLA.

8k:	#EXROM=0, #GAME=1 : start $8000-$9FFF ROML(8k)
8k ultimax:	#EXROM=1, #GAME=0 : start $E000-$FFFF ROML(8k) (replaces kernal ROM)
16k:	#EXROM=0, #GAME=0 : start $8000-$BFFF (ROML) + $A000-$BFFF (ROMH)
16k ultimax:	#EXROM=1, #GAME=0 : start $8000-$9FFF (ROML) + $E000-$FFFF (ROMH)

To find these settings in a .CRT file, use WinVICE's cartconv.exe tool with the -f option.

C:\WinVICE-2.4-x86>cartconv -f Wizard_of_Wor.crt / CRT Version: 1.0 / Name: Wizard of Wor / Hardware ID: 0 (Generic Cartridge) / Mode: exrom: 0 game: 0 (16k Game) / offset sig type bank start size chunklen / $000040 CHIP ROM #000 $8000 $4000 $4010
Finding mode for Wizard of Wor in a CRT file.

# Converting .CRT to .BIN
The eprom must be burned with the binary file. Use the WinVICE's cartconv.exe tool to generate the binary file.

C:\WinVICE-2.4-x86>cartconv -i Wizard_of_Wor.crt -o wizardofwor.bin / Input file : Wizard_of_Wor.crt / Output file : wizardofwor.bin / Conversion from Generic Cartridge .crt to binary format successful.
Converting CRT to BIN for the EPROM.

# Solder Jumpers
In cases where you just want a fixed game or dead test cart, you don't need the jumper headers and the dipswitch.

solder jumper settings	#EXROM	#GAME	switch	16K	16K	#ROML	#ROMH
mode	JP5	JP4	JP6	JP7	JP1	JP2	JP3
8k	x		x			x
8k ultimax		x	x				x
16k	x	x		x	x
16k ultimax		x		x	x

# Bill of Materials (BOM)